| Product Details – 1 |
| --- |
| Name | Prakash Torch |
| Technical Data |  |
|  | Dimensions | 85 x 41 x 20mm (L x W x H) |
|  | Weight | 60 g |
|  | Wattage | 0.8 Watt |
|  | Battery | 9V (use and throw) |
|  | LED | 10mm White LED |
|  | Light Dispersion | 30 deg |
|  | Light Intensity | 200 Lux |
| Features | High ease of use for people of all ages |
|  | 50 hours back up |
|  | White focus provides steady, bright light |
|  | Water proof |
|  | Very easy to change the battery |
|  | No loose contact |
| Operating Conditions | 9V DC |
|  | 0°C to 50°C |

Prakash Torch

| Product Details – 2 |
| --- |
| Name | Prakash Torch |
| Technical Data |  |
|  | Dimensions | 85 x 41 x 20cm (L x W x H) |
|  | Weight | 55 g |
|  | Wattage | 0.8 Watt |
|  | Battery | 9V (use and throw) |
|  | LED | Super Flux LED |
|  | Light Dispersion | 130 deg |
|  | Light Intensity | 132 Lux |
| Technological Features | High ease of use for people of all ages |
|  | 50 hours back up |
|  | Wide angle of LED, reduces strain on eyes. |
|  | Water proof |
|  | Very easy to change the battery |
|  | No loose contact |
| Operating Conditions | 9V DC |
|  | 0°C to 50°C |

Prakash Torch (Super Flux LED)

| Product Details – 3 |
| --- |
| Name | Emergency Lamp |
| Technical Data |  |
|  | Dimensions | 287 x 110 x 79mm (L x W x H) |
|  | Weight | 1.2 kg |
|  | Wattage | 1.25 watt |
|  | Battery | 6V Rechargeable |
|  | LED | 18 Super Flux LEDs |
|  | Light Dispersion | 130 deg |
|  | Light Intensity | 160 Lux |
| Technological Features | High ease of use for people of all ages |
|  | Handle bar on top for easy mobility |
|  | White focus provides steady, bright light |
|  | Easy access slide button on top for low light situations |
|  | 30 hrs back up provides long life and infrequent need for charging |
|  | Durable acrylic casing available in different colors (Blue, Red, yellow, White, Pink) |
|  | Charging indicator lets user know the battery is receiving charge |
|  | Battery warranty of 6 months |
| Operating Conditions | 6V DC. Dry battery, Maintenance Free. |
|  | 0°C to 50°C |
|  | Charges on 230V AC |

Emergency Lamps

| Product Details – 4 |
| --- |
| Name | Kisan Torch |
| Technical Data |  |
|  | Dimensions | 192 x 120 x 140mm (L x W x H) |
|  | Weight | 1.0 kg |
|  | Wattage | 0.5 watt (10 mm LED); 0.1 watt (Super Flux LED) |
|  | Battery | 6V Rechargeable |
|  | LED | 8 10 mm LEDs; 2 Super Flux LEDs |
|  | Light Dispersion | 60 deg |
|  | Light Intensity | 420 – Lux (Front) & 420 – Lux (Side) |
| Technological Features | High ease of use for people of all ages |
|  | Handle bar on top for easy mobility |
|  | White focus provides steady, bright light |
|  | Two types of light for optimal usage in low light situations |
|  | 34 hours back-up provides long life and infrequent need for charging |
|  | Durable casing available in different colors (yellow, white, red) |
|  | Charging indicator lets user know the battery is receiving charge |
|  | Battery warranty of 6 months |
| Operating Conditions | 6V DC. Dry battery, Maintenance Free. |
|  | 0°C to 50°C |
|  | Charges on 230V AC |

Kisan torch

| Product Details – 5 |
| --- |
| Name | LED Strip |
| Technical Data |  |
|  | Dimensions | 192 x 120 x 140mm (L x W x H) |
|  | Weight | 400 g |
|  | Wattage | 1.3 watt |
|  | Battery | 12V Rechargeable |
|  | LED | 21 Super Flux LEDs |
|  | Light Dispersion | 160 deg |
|  | Light Intensity | 340 Lux |
| Technological Features | High ease of use for people of all ages |
|  | White focus provides steady, bright light |
|  | Easy to fix on ceilings, walls, or table-tops |
|  | Durable casing made of sturdy plastic |
|  | Can be used inside of houses or on vehicles |
| Operating Conditions | 12V DC |
|  | 0°C to 50°C |

LED Strip

| Product Details – 6 |
| --- |
| Name | 12V DC Bulb |
| Technical Data |  |
|  | Dimensions | 35 x 35 x 50mm (L x W x H) |
|  | Weight | 100 g |
|  | Wattage | 2 watt |
|  | LED | 6 Super Flux LEDs |
|  | Light Dispersion | 140 deg |
|  | Light Intensity | 286 Lux |
| Technological Features | Low power consumption |
|  | White focus provides steady, bright light |
|  | Easy to fix in DC Holder |
|  | Durable and compact casing |
|  | Works on 12V DC |
| Operating Conditions | 12V DC (170mA minimum) |
|  | 0°C to 50°C |
|  | 2 Watts/hour |

12V DC Bulb

| Product Details – 7 |
| --- |
| Name | 6V DC Bulb |
| Technical Data |  |
|  | Dimensions | 35 x 35 x 50mm (L x W x H) |
|  | Weight | 100 g |
|  | Wattage | 0.5 watt |
|  | LED | 6 Super Flux LEDs |
|  | Light Dispersion | 140 deg |
|  | Light Intensity | 200 Lux |
| Technological Features | Low power consumption |
|  | White focus provides steady, bright light |
|  | Easy to fix in DC Holder |
|  | Durable and compact casing |
|  | Works on 12V DC |
| Operating Conditions | 6V DC (83mA minimum) |
|  | 0°C to 50°C |
|  | 0.5 Watts/hour |

6V DC Bulb

| Product Details – 8 |
| --- |
| Name | LED AC Bulb |
| Technical Data |  |
|  | Dimensions | 35 x 35 x 50mm (L x W x H) |
|  | Weight | 100 g |
|  | Wattage | 1 watt |
|  | LED | 6 Super Flux LEDs |
|  | Light Dispersion | 140 deg |
|  | Light Intensity | 200 Lux |
| Technological Features | Low power consumption |
|  | LED-usage provides long life without compromising on brightness |
|  | Useful in areas of low or non-existent light sources, |
|  | Small white compact casing provides for high durability |
|  | Can be placed in existing grid without the need for extra batteries |
|  | Weather and shock resistant for use in harsh environments |
| Operating Conditions | 230V AC |
|  | 0°C to 50°C |
|  | 1 Watt/hour |

LED AC Bulb