## Slide 1: Learning about calorific value of a fuel

## Slide 2: Calorific value
Lets us prepare a recipe using different fuel types to learn this concept

## Slide 3: What will be the cost impact If the same recipe is prepared using three different fuels ?
To find this we need to observe or find out following things during our practical –
  Time taken for cooking a recipe
  Quantity of fuel consumed
  Quantity of food (recipe) cooked.
  Total Cost of each fuel which is consumed

## Slide 4: Observations found during trial in Mangaon school
Materials used during trial :
  Planned recipe – 1 kg of “Khichadi” :
  Ingredients used : 1 kg of rice with oil & some vegetables like onions, tomatoes, coriander leaves, green chili pest, spices, salt, etc.
  Type of fuels used for cooking :
Wood –Chula, cooking gas , kerosene - stove

## Slide 5: Observations found during trial in Mangaon school
Below table indicates time taken for cooking 1 Kg of “Khichadi” using three different fuels :
Source | Time taken for cooking | Fuel Consumed
Wood | 42 min | 1.9 Kg
Kerosene | 45 min | 200 ml
Cooking gas | 45 min | 200 gm

## Slide 6: Why we need different quantity of fuel to cook same amount of “Khichadi” ?

## Slide 7: CALORIFIC VALUE OF FUEL
Definition of the calorific value :
It can be defined as the amount of heat liberated in
Kcal for the complete combustion of 1 Kg of fuel.

## Slide 8: Calorific values of different fuels.
Sr. No. | Name of the Fuel | Approx heating value Kcal/Kg | 
 |  | Natural State | Dry State
1 | Wood | 1500 | 3500
2 | Cattle dung | 1000 | 3700
3 | Kerosene |  | 10000
4 | Bio gas (12 kg of dung produces 1cu. mtr gas.) |  | 4700 - 6000
5 | Natural Gas |  | 8600
6 | Coal |  | 4000- 7000

## Slide 9: Calculation of Calorific values to cook “Khichadi” using different fuels ?
Name of the Fuel Fuel consumed * Calorific values = Calories used for preparing . “Khichadi”
1)Wood 1.9 Kg * 3500 = 6650 Kcal
2)Kerosene 0.200 ml * 10000 = 2000 Kcal
3)Gas 0.200 gm * 8600 = 1720 Kcal

## Slide 10: Calorific value efficiency
Wood - Low
Cooking gas - High
Kerosene – Medium
Learning : It is observed that because of low calorific efficiency wood quantity got highly consumed compared to cooking gas and kerosene

## Slide 11: Costing of fuel
For this we need to consider the quantity of fuel consumed for preparation of “Khichadi” and market cost of the fuel
Fuel Source | Fuel Consumed | Market Cost in Rs | Total Cost on fuel in Rs
Wood | 1.9 Kg | 5 Rs/Kg | 9.5 Rs
Kerosene | 200 ml | 20 Rs./ ltr | 4 Rs
Cooking gas | 200 gm | 38 Rs. / Kg | 7.6 Rs

## Slide 12
Which fuel is costly ?
Which is the best option to use ?
What type of fuel are easily available ?

## Slide 13: Thanks