## Slide 1: How to use a Dumpy Level Example 1
Find the difference in height between the benchmark and the top of the slope
Top of Slope
?
Divide hill into 3 spots to make easier
Otherwise too far to see or leveling staff not long enough

## Slide 2: How to use a Dumpy Level Example 1
9mAOD (above sea level)
Back sight

## Slide 3: How to use a Dumpy Level Example 1
Rotate Dumpy round
Back sight
9mAOD (above sea level)
Move Level to new position
2m
Foresight
2mAOD (above sea level)
Foresight

## Slide 4: How to use a Dumpy Level Example 1
Move Dumpy to new position
9mAOD
Back sight
2mAOD
Foresight
6mAOD
Back sight

## Slide 5: How to use a Dumpy Level Example 1
Rotate Dumpy round
to new position
9mAOD
Back sight
2mAOD
Foresight
6mAOD
Back sight
Move Level to new position

## Slide 6: How to use a Dumpy Level Example 1
9mAOD
Back sight
2mAOD
Foresight
6mAOD
Back sight
1mAOD
Foresight

## Slide 7: How to use a Dumpy Level Example 1
9mAOD
Back sight
2mAOD
Foresight
6mAOD
Back sight
1mAOD
Foresight
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
Bench mark | 913 | 9 | 922 | 2 | 920
 | 920 | 6 | 926 | 1 | 925
9m
913m + 9m
2m
6m
6m + 920m
1m
Level of dumpy = 922m
Level of dumpy = 926m

## Slide 8: How to use a Dumpy Level Example 1
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
Bench mark | 913 | 9 | 922 | 2 | 920
 | 920 | 6 | 926 | 1 | 925
So the difference in height is
925m-913m=12m
?

## Slide 9: Example 2
I want to construct a water pipe on the hill?
B
C
D
To find the pressure that will result from the pipe
I need to know the height difference between point A and point D
A= 875mAOD

## Slide 10: Example 2
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
Benchmark | A=875 |  |  |  | B=
 | B= |  |  |  | C=
 | C= |  |  |  | D=
B
C
D
A= 875mAOD

## Slide 11: Example 2
A= 875mAOD
B
C
D
9m
4m
Level of dumpy=879mAOD
1m
Level of dumpy=871mAOD
B= 870mAOD
11m
C= 860mAOD
2m
Level of dumpy=862mAOD
12m
D= 850mAOD

## Slide 12: Example 2
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
Benchmark | A=875 | 4 | 879 | 9 | B= 879-9=870
 | B= 870 | 1 | 871 | 11 | C= 871-11=860
 | C= 860 | 2 | 862 | 12 | D= 862-12= 850

## Slide 13: Example 2
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
Benchmark | A=875 | 4 | 879 | 9 | B= 879-9=870
 | B= 870 | 1 | 871 | 11 | C= 871-11=860
 | C= 860 | 2 | 862 | 12 | D= 862-12= 850
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
 | D=850 |  |  |  | C=
 | C= |  |  |  | B=
 | B= |  |  |  | A=
Once you have gone down the hill,
check you answer by coming back up the hill

## Slide 14: Example 2
B
C
D
9m
4m
Level of dumpy=879mAOD
1m
Level of dumpy=871mAOD
B= 870mAOD
11m
C= 860mAOD
2m
Level of dumpy=862mAOD
D= 850mAOD
12m
A= 875mAOD

## Slide 15: Example 2
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
Benchmark | A=875 | 4 | 879 | 9 | B= 879-9=870
 | B= 870 | 1 | 871 | 11 | C= 871-11=860
 | C= 860 | 2 | 862 | 12 | D= 862-12= 850
 | Ground Level | Backsight (from Dumpy Level) | Height of instrument (Ground Level + Backsight from Dumpy Level) | Foresight (from Dumpy Level) | Height of new point (Height of instrument-foresight)
 | D=850 | 12 | 862 | 2 | C=862-2=860
 | C=860 | 11 | 871 | 1 | B=871-1=870
 | B=870 | 9 | 879 | 4 | A=879-4=875
Once you have gone down the hill,
check you answer by coming back up the hill

## Slide 16: Example 2
B
C
D
A= 875mAOD
A= 850mAOD
Change in height= 25m
So what was the change in height?

## Slide 17: Summary Questions
What is a Dumpy Level Used for?
What 2 things can you use to check if things are level?
How does a spirit level work?
One you have done a backsight reading what would you do next with a dumpy level?