## Slide 1: Plane Table Surveying

## Slide 2
Chose a location where you can see all other points of interest
Pace out the area so that you get a feel for what kind of scale you may use.
Set up tripod over this location and get as level as possible
Put on drawing board and ensure level
Secure drawing sheet to the drawing board
Pivot drawing board so that the top of the sheet is aligned with and north and mark on
Mark central point of drawing sheet and apply the plumb line.
Place the alidade on the drawing board with the end with the narrow slit towards your eye and align it so that the rule touches the central point.
Draw a line along the rule in the direction of this point.
Measure the distance from the plumb line to the point of interest. Use a suitable scale to mark on this distance on your drawing sheet.
These are the steps you must follow in order to carry out an accurate plane table survey:

## Slide 3: Methods of Plotting
Radiation
B
C
A
P
Chose a point that you can
see all required positions
Notes: Radiation:
Select appoint p so that all point to be located are visible from it.
Set up the table at p and leveled.
Marked the direction of magnetic meridian with through compass in top corner of sheet.
Select the point p on the sheet so that it is exactly over station p on the ground.
Centering the Alidades on p, sight the various points A, B, C etc. and draw the rays along edge of Alidades.
Measure the distance PA, PB, PC etc. from p to various point with chain or tape and plot them to scale along the co responding rays. Join the points a, b, c, etc. to give outline of survey.

## Slide 4: Methods of Plotting
Radiation
B
C
A
P
Chose a point that you can
see all required positions
Measure with a tape
A
N
7cm
A
70m

## Slide 5: Methods of Plotting
Radiation
B
C
A
Measure with a tape
A
70m
N
7cm
A

## Slide 6: Methods of Plotting
Radiation
B
C
A
Measure with a tape
A
70m
50m
B
5cm
N
7cm
A
Notes: Radiation:
Select appoint p so that all point to be located are visible from it.
Set up the table at p and leveled.
Marked the direction of magnetic meridian with through compass in top corner of sheet.
Select the point p on the sheet so that it is exactly over station p on the ground.
Centering the Alidades on p, sight the various points A, B, C etc. and draw the rays along edge of Alidades.
Measure the distance PA, PB, PC etc. from p to various point with chain or tape and plot them to scale along the co responding rays. Join the points a, b, c, etc. to give outline of survey.

## Slide 7: Methods of Plotting
Radiation
B
C
A
Measure with a tape
A
70m
50m
B
5cm
N
7cm
A
40m
4cm
C

## Slide 8: Methods of Plotting
Radiation
A
B
5cm
N
7cm
A
4cm
C
P
1:1000

## Slide 9: Methods of Plotting
Radiation
A
B
N
A
C
P
1:1000

## Slide 10: What could we use this map for?
A farmer wants to know how big his field is so he knows how much seed to buy.
How will he work out how many bags of seed he will need?
You must find the area of the field from the scale drawing
Convert it using the scale into the real life area
Divide this area by the area 1 bag of seed will cover
1 bag of seed will cover 0.5m2

## Slide 11: What could we use this map for?
Radiation
A
B
N
A
C
P
1:1000
The area of a triangle can be found by 0.5xhxb
h=9cm
b=8cm
The area of a square is hxb
9x8 = 72 =36 cm2
2 2

## Slide 12: What could we use this map for?
Radiation
B
N
A
C
P
1:1000
As the scale is 1:1000
36 cm2 on the map=36cm2 x 1000 in real life
So in real life the area is 36000cm2
Or 3.6m2
So as 1 bag of seed will cover 0.5m2
We will need
3.6m2 = 7.2 bags of seed
0.5m2
So the farmer will need to buy 8 bags of seed to cover his field.

## Slide 13: Other examples of Radial Plotting
Notes: http://www.slideshare.net/Azil14/plane-table-in-surveying