## Slide 1: Circuits
Energy & Environment

## Slide 2: Simple Circuit
G
-ve
+ve
Wire
Lamp
Switch
Fuse
Battery
Power Source
Safety Device
Controlling Device
Purpose
Connect circuit together
Electricity to Light
What symbols are shown here and what do they do?

## Slide 3: Closed Circuit
G
-ve
+ve
For current to flow round circuit, must be a connecting path
Low resistance
Some
resistance
Potential difference
Potential difference
Where is there potential difference & where is there resistance?

## Slide 4: Open circuit
G
-ve
+ve
Current stops as doesn’t have a complete path
Examples of open circuit
Very high resistance
No power used
Where is there potential difference & where is there resistance?

## Slide 5: Short Circuit
G
-ve
+ve
Almost no
resistance
Some resistance
Why does the current chose to go this way?
Results in excessive current
Which can cause overheating and damage.
Circuits are protected against excessive current by fuses
Notes: .

## Slide 6: Series Circuit
G
-ve
+ve
Where could we put this bulb if we want to add it in series?

## Slide 7: Series Circuit: Current
G
-ve
+ve
If the current through the switch is 4 amps, what is the current through the light bulb A and B?
A
B
=4 amps
=4 amps
Current through switch=4 amps
In a series circuit the current is the same across the circuit
Itotal=I1=I2=I3

## Slide 8: Series Circuit: Voltage
G
-ve
+ve
A
B
=6 volts
=6 volts
EMF= 12 volts
In a series circuit the voltage is the sum of the EMF
The potential difference in EMF across two points is called the potential difference.
A
B
12 volts
12 volts=6 +6
This side
This side
(EMF)vtotal=V1+V2+V3

## Slide 9: Series Circuit: Voltage
G
-ve
+ve
A
C
=4 volts
=4 volts
EMF= 12 volts
In a series circuit the voltage is the sum of the EMF
What happens when we add another bulb? What is the voltage of each identical bulb.
A
B
12 volts
12 volts
This side
This side
B
=4 volts
12 volts= 3 x light bulbs
Light bulb = 12 volts
3
=4 volts each
(EMF)vtotal=V1+V2+V3

## Slide 10: Series Circuits
If this bulb blows what happens to the other bulbs?
The circuit is open so there is no path for the current to travel.
If current=0
Power=0
As power=EMF x Current

## Slide 11: Parallel Circuit
G
-ve
+ve
Where could we put this bulb if we want to add it in parallel?

## Slide 12: Parallel Circuit: Current
G
-ve
+ve
In a parallel circuit the current is split up throughout the different branches
If the current through the switch is 4 amps, what is the current through the identical light bulbs A and B?
=2 amps
=2 amps
Current through switch=4 amps
A
B
Itotal=I1+I2+I3
Notes: Need to work this out why

## Slide 13: Parallel Circuit: Voltage
G
-ve
+ve
Voltage in parallel circuits is equal across branches
Voltage
=1.5 volts
A
B
1.5 volts
The potential difference in EMF across two points is called the potential difference.
A
B
1.5 volts
A
B
1.5 volts
This side
This side
1.5 volts

## Slide 14: Parallel Circuit: Voltage
G
-ve
+ve
Voltage in parallel circuits is equal
Voltage
=1.5 volts
A
B
1.5 volts
A
B
1.5 volts
A
B
1.5 volts
A
B
1.5 volts
What happens when we add another bulb?
(EMF)vtotal=V1=V2=V3
This side

## Slide 15: Parallel Circuits
The circuit for that bulb is open but the circuit for the other two bulbs is ok
If this bulb blows what happens to the other bulbs?