## Slide 1: Energy Audits & Electricity Bills
Energy & Environment

## Slide 2: Increasing Energy Demand
What does this graph tell you?
India’s energy consumption has been increasing at one of the fastest rates in the world.
Population growth
Economic Development
This is due to:

## Slide 3: Increasing Energy Demand
What do these graphs tell you?
Supply is less than Demand
Need imports to meet the demand
There is an urgent need to reduce energy requirements
This can be achieved through conserving energy

## Slide 4: Advantages of Conserving Energy
Reduce Power cuts
Will help make power available to all
Will make India more independent from fossil fuel rich countries
Reduce pollution
Save money
To conserve energy we need to find out where we are wasting it.
We can find this out by completing an energy audit

## Slide 5: Energy Audit
An energy audit helps you to calculate how much energy you use and where it is used.
This allows you to identify where you could make savings in your energy consumption
Notes: Beyond simply identifying the sources of energy use, an energy audit seeks to prioritize the energy uses according to the greatest to least cost effective opportunities for energy savings
What they are
What used for
Why useful

## Slide 6: How to carry out an energy audit
1. Set your boundaries
Electrical Wattage consumed by equipment is normally written on its name plate
2. Find out energy consumed by every application
3. To calculate the energy consumed by an appliance, multiply the power rating of the appliance by the time of consumption

## Slide 7: Energy Consumed
This is a 40W light bulb
Calculate the monthly energy consumption in KW Hours
Its on between 7pm and 12am every day

## Slide 8: Energy Consumed
Consumption per day = wattage x daily use
= 40W x (12-7) hours
= 40W x 5 hours
=200 watt hours
Consumption per month = wattage per day x no of days in 1 month
= 200 watt hours x 30
= 6000 watts hours
= 6KW hours
1KWH = 1 unit of electricity
So 6 units of electricity are used by the bulb in a month.
What could you do to reduce this amount of electricity consumed?
Notes: Figures from curriculum. Need to check electricty bill?
User (residential, industry, commerical, government, military....) Total usage over year (kwhs) Peak and average demand (kW) Time of usage patterns (day/night, peaking/steady...) Location (utility service, governenment) Service Type (secondary (480v), primary (12,600v), transmission (50,000v), substation.....)

## Slide 9: Conserving Energy
Use a CFL bulb
(reduced Watts)
Turn the light off if you don’t need it all 5 hours
Invest in a solar lamp

## Slide 10: Energy Consumed
Electricity provider
So how much does 6 units of electricity cost?
?
Depends on:
Time of day
What type of customer you are

## Slide 11: Electricity Bills
Tariff Category | Demand Charges (Rs./ KVA/ Month) | Energy Charges paise/ KWH | slot 1 | slot 2 | slot 3 | slot 4
 |  |  | (22.00 to 6.00) | (06.00 to 9.00) and (12.00 to 18.00) | (9.00 to 12.00) | (18.00 to 22.00)
HT-1 Industries Continous (on express feeder) | 150 | 527 | -85 | 0 | 80 | 110
HT-V Agriculture | 25 | 215 | 0 | 0 | 0 | 0
LT-V Industrial 0-20KW | 150 per connection per month | 390 | 0 | 0 | 0 | 0
Vigyan Ashram
Why do you think there are different time slots?
Why do you think there are different charges?

## Slide 12: Energy Consumed
1 unit of electricity= Rs.3.9
What is the monthly cost of this light bulb?
6 units
x Rs 3.9
Rs 23.4
So how much does 6 units of electricity cost?

## Slide 13: Energy Audit Exercise 1
To do this we can carry out an energy audit for this room.
As theoretical lessons with Powerpoint are new to Vigyan Ashram we need to calculate how much extra energy will be consumed.
We can then calculate the % increase in a monthly bill.
?

## Slide 14: Energy Audit Exercise 1
So what information do we need?
Equipment & Power need
Duration of use
Price of unit
Time of day?
Tariff Category | Demand Charges (Rs./ KVA/ Month) | Energy Charges paise/ KWH | slot 1 | slot 2 | slot 3 | slot 4
 |  |  | (22.00 to 6.00) | (06.00 to 9.00) and (12.00 to 18.00) | (9.00 to 12.00) | (18.00 to 22.00)
HT-1 Industries Continous (on express feeder) | 150 | 527 | -85 | 0 | 80 | 110
HT-V Agriculture | 25 | 215 | 0 | 0 | 0 | 0
LT-V Industrial 0-20KW | 150 per connection per month | 390 | 0 | 0 | 0 | 0
Present these findings in a table

## Slide 15: Energy Audit Exercise 1
Equipment | Wattage (watts) | Per day usage (hrs) | Per day consumption (KW Hours) | Per month consumption = Per day usage * 26 days | Electric bill = Monthly usage (KWH) * per unit rate (Rs.3.9 per unit)
 |  |  |  | Total | 
How many days should we include in a month?
How do we find out what a unit of electricity costs?
On average there are 30 days in a month. But we have Saturdays off. So assume 4 Saturdays in each month.
30-4=26
Tariff Category | Demand Charges (Rs./ KVA/ Month) | Energy Charges paise/ KWH | slot 1 | slot 2 | slot 3 | slot 4
 |  |  | (22.00 to 6.00) | (06.00 to 9.00) and (12.00 to 18.00) | (9.00 to 12.00) | (18.00 to 22.00)
HT-1 Industries Continous (on express feeder) | 150 | 527 | -85 | 0 | 80 | 110
HT-V Agriculture | 25 | 215 | 0 | 0 | 0 | 0
LT-V Industrial 0-20KW | 150 per connection per month | 390 | 0 | 0 | 0 | 0

## Slide 16: Energy Audit Exercise 1
What energy consuming appliances are there?
65 watts
180 watts
2 x 35 watts

## Slide 17: Energy Audit Exercise 1
How long will they be on for today?
2 hours
2 hours
2 hours

## Slide 18: Energy Audit Exercise 1
Equipment | Wattage (watts) | Per day usage (hrs) | Per day consumption (KW Hours) | Per month consumption = Per day usage * 26 days | Electric bill = Monthly usage (KWH) * per unit rate (Rs.3.9 per unit)
Lap top | 65 | 2 | 0.13 | 3.38 | 13.182
Projector | 180 | 2 | 0.36 | 9.36 | 36.504
Light | 35 | 2 | 0.07 | 1.82 | 7.098
Light | 35 | 2 | 0.07 | 1.82 | 7.098
 |  |  | Total | 16.38 | 63.882

## Slide 19: Energy Audit Exercise 1
If we look at Vigyan Ashram’s old bill we can calculate % increase in units and cost that this will cause.
See Electricity Bill Here
% increase= increase in units
original units
% increase = 16.38 x 100= 7.38% increase in units
222 1
So the school used 222 units last month
Will it be a 6.56% increase in price too?
Less due to fixed charges

## Slide 20: Energy Audit Exercise 1
From looking at the Energy Audit table, which factor has the greatest impact?
How could we reduce the energy consumption of this?
Reduce time that it is on

## Slide 21: Energy Audit Exercise 2
Can you help Vigyan Ashram reduce its energy bill?
Split into pairs and carry out an energy audit of Vigyan Ashram
Cow shed
Office
Kitchen & Fablab
DST
Energy & Environment
Engineering
Agriculture
Guest house
Classroom
Girl’s Accommodation
Boys’s Accommodation
Water Pump
Amma’s
Anan’s
Foodlab

## Slide 22: Energy Audit Exercise 2
Equipment | Wattage (watts) | Per day usage (hrs) | Per day consumption (KW Hours) | Per month consumption = Per day usage * ?? days | Electric bill = Monthly usage (KWH) * per unit rate (Rs.3.9 per unit)
 |  |  |  | Total | 
This will change depending on what you are measuring

## Slide 23: Energy Audit Exercise 2
How does your estimate compare to Vigyan Ashram’s last electricity bill?
What and where are the big users of electricity?
How could we reduce this energy consumption?
Reduce time used
Turn off appliances when not in use
Only use lights when needed
Think of other ways of powering what we need
Notes: Identify the most likely area of energy wastage
Now you know energy consumption and cost incurred on various appliances. Please find out possible alternatives to save energy. Following are tips to identify energy saving areas –

## Slide 24: Energy Audit Exercise 2
Make an action plan for immediate action that requires no cost.
How can we communicate these to the rest of the school?
Create a long term plan of what could be done at Vigyan Ashram to reduce its electricity consumption
e.g. wind power for pumping water.
Could these be your future energy & Environment projects?
Notes: 4

## Slide 25: Energy Audit
How could you do this?
Keep a review of the savings over the next few months
Old Bills
Plot a graph of energy consumption over a year
Chart: Electricty Units
| January | February | March | April | May | June | July | August | September | October | November | December
 | 222 | 256 | 342 | 234 | 123 | 324 | 345