## Slide 1: Wires & Cables
Energy & Environment

## Slide 2: Conductors
-
-
-
-
High Resistance
-
-
-
-
-
-
-
-
-
-
-
-
-
Low Resistance
A conductor has many free electrons so is good at transferring electrical current
Good Conductor
Bad Conductor
Conductance is the opposite of resistance
It is measured in ‘Mho’s (ohm backwards) ℧

## Slide 3: Different types of conductors
Material Used
Copper
High conductivity
Easily soldered
Heavier & more expensive than aluminum
Copper used in house wiring
1mm2, 1.5mm2
4mm2 , 6mm2
Aluminum
60% conductivity of copper
Cheap & lighter than copper
Lowest conductivity
Heavier than aluminum
Galvanized Iron (GI)
Used in overhead lines

## Slide 4: Different types of conductors
Respective of their property
Good Conductors
Bad Conductors
Medium resistance
Used for converting electrical energy into heat, light & sound
PVC, glass
High resistance
Non Conductors
Carry current
Low resistance
Copper & Aluminum
Tungsten & Nichrome
Insulators
Wires & cables use conductors & non conductors to their advantage

## Slide 5: Different types of conductors
Physical Appearance
Solid Conductor
Used in cables.
e.g. copper, aluminum, steel
Stranded Conductor
Flexible
1.13 to 3.73 mm diameter
1, 7, 19, 37 stands
Multi stranded Conductor
0.2 or 0.3 mm diameter
14, 22, 24,84 strands
Flexible Conductor
14, 23, 40 strands
<0.2 mm diameter

## Slide 6: Wires & Cables
Wires
Domestic & small industry wiring
In appliances
Cables
Small & big industries
Distribution Lines
Transmission lines
The size & type of wire/cable must suit the power rating required for their use. The higher the power the thicker the wire/cable
Wires & Cables are purpose built conductors

## Slide 7: Types of wires
Vulcanized India Rubber (VIR)
suitable for: low & medium voltage supply only
tinned copper/ aluminum
Cotton tape & cotton braiding
Bitumen
Vulcanized India Rubber (VIR)
To protect against corrosion from the VIR
Old type: not readily available to purchase

## Slide 8: Types of Wires
Cabe Tyre Sheath wire (CTS)
tinned copper
Rubber/plastic
Thicker Rubber/plastic
Don’t absorb moisture
Available in 250/440V only
Old type: not readily available to purchase
Notes: .

## Slide 9: Types of Wire
PVC Wire
copper/ aluminum
Polyvinyl chloride (PVC)
Widely used
Long life
Durable against water, heat, oil, UV light
Available in 600, 660, 1100 Voltage

## Slide 10: Wiring Appliances
Earth
Takes current to ground if appliance has fault
Live
Provides current to appliance
Neutral
Returns current to power source
What wire is missing and why?
What do each of these wires do?

## Slide 11: Standard Wire Gauge & Current Carrying Capacity
Higher current will heat the cable and damage the insulation and may result in short circuit
Each number represents a size of wire
Maximum safe current that can flow through a cable

## Slide 12: Cables
Larger sized conductors
Type of insulation
Types of cable are sorted by:
Cotton covered
Silk coated
Asbestos covered
Rubber coated
PVC coated
Type of conducting material
Their shape
Unarmored
Armored
Voltage Grade
Low
High
Copper
Aluminum
Mechanical protection
Flat
Round

## Slide 13: Splices & Terminals
Splices or terminals must be used at termination points
These must be as mechanically & electrically strong as the conductor or device which it is used.
When a cable enters into an accessory its called a termination.
Types
Washers
Pillar terminals
Screw heads & nuts

## Slide 14: Summary Questions
Why might you use aluminum in wire instead of copper?
What are some advantages of PVC wire?
Why might you use ‘bad’ conductors in a circuit?
Why is it important not to supply a cable with more current than its current carrying capacity?